## Slide 1: Real-time RFID Cloning in the Field

## Slide 2: Who am I
Dennis Maldonado (@DennisMald)
Adversarial Engineer @ LARES Consulting
Founder
  Houston Locksport
  Houston Area Hackers Association (HAHA)
DEFCON 23 – Hacking Access Control Systems
DEFCON 24 – Sticky Keys to the Kingdom

## Slide 3: RFID
Radio Frequency Identification

## Slide 4: Radio Frequency Identification (RFID)
Electronic Access Control for many companies
Contactless authentication
125 kHz Low-Frequency (LF) - HID Prox, Indala, flex, ioProx, etc.
13.56 MHz High-Frequency (HF) - HID iCLASS, MIFARE, LEGIC, etc.
Credentials = cards, tags, stickers, key fobs, etc.

## Slide 7: Long Range Readers

## Slide 8: Long Range Reader
MaxiProx 5375
  Reads HID Prox Cards
  Read Range: 18-24 inches
R90
  Reads HID iCLASS cards
  Read Range 12-16 inches
Small enough to hide in a backpack
Find them on eBay

## Slide 11: Modified Long Range Reader
Battery Source
  Run the reader from batteries
Raspberry Pi Zero W
  Allow for connectivity via wireless
  Support for web page, android apps, etc
  Communicate with other devices for automatic cloning
  Automatically interpret and decode badge reads

## Slide 12: Demo

## Slide 13: Making your own

## Slide 14: Making your own Long Range Reader
Battery Source
  Supports 3 Amps
  18650 Batteries
  Protection circuit recommended
DC Boost Converter
  Boost voltage if battery source is not at least 12v
DC Buck Converter
  Step down battery voltage to 5v for the Raspberry Pi
Raspberry Pi Zero W
Wire

## Slide 15: Raspberry Pi Zero W
Raspbian Jessie Lite
WI-FI Access Point
Python Code and setup script
  https://github.com/linuz/LongRangeReader

## Slide 16: Automated Cloning
Raspberry Pi 3 or Raspberry Pi Zero W
  Raspbian Jessie Lite
  Proxmark3 software
USB Battery Pack
Proxmark 3

## Slide 17: Questions?